Panel Protector / Hardwire / PTS 120 H / 2nd Edition

# Specifications - Operating:

Maximum Operating Voltage:				120 Volts AC

Typical Leakage Current:					<5µ amps

Operation Temperature:					- 40 to +85°C

Connectors:							Hardwired

### Lines Protected:						L-N, N-G, L-G

Installation Configuration:					Parallel

# Specifications - Electronic:

Maximum Surge Current (8x20µs):				100,000 Amps Total

Maximum Surge Voltage (1.2x50µs):			10,000 Volts

Capacitance:							<2,000 pf

Clamping Voltage:						130 Volts RMS

Clamping Response Time:					<5 nanoseconds

Current:							Non-Load Bearing

Voltage:							Voltage Sensitive

Design:							Thermally Fused Hybrid

Operation Indicators:						Light Emitting Diode (LED)

Power Dissipation (8x20µs):					13,000,000 Volts Amps

Energy Dissipation:						950 Joules

UL 1449:							1449 Second Edition

UL Recognized Component:					File E121637

USL and CNL Approved:					United States / Canada

Dimension:							Depth 2.25"

Width 2.844"

Length 5.694” (including tabs)

Weight: 							Approximately 1lbs.

Pass Voltage Tested to ANSI/IEEE B3 Impulse:		UL’s Best 330 V Peak Rating

E-Clips surge suppressors have a Lifetime Product Warranty.  Please see warranty statement for complete product warranty information.

888-471-1038 Toll Free