Data Line Protectors

Data Line Protectors are available for Arcnet, AS400, BNC, Control Line, Ethernet, LAN, Risc, RS232, Token Ring, 10-Base-T, or any low voltage AC or DC signal circuits requiring protection. Terminations are available for almost any computer with stand off voltage from 5V to 200V. All Data Line Protections are non load-bearing.

Data Line

RS2321DB25

RS422/DB9

RJ45110 BASE T

BNC C

DLP TX

CL DC TWP

D2W TB-N

D DUAL 4W

D DUAL 2W

D DUAL 4W

Peripheral pins 1-9, 19 & 20 protected

w/ DB 25 Connector

Peripheral w/ DB 9 Connector

Network/Terminal Protector

Network Coaxial Cable Protector

Twinax/IBM 34, 38 etc.

Network Twisted Pair*

Data Line Protector w/ Single

Terminal Block & lPair - Network*

Data Line Protector w/ Single Terminal

Block & 2 Pair - Network~

Data Line Protector w/ Dual

Terminal Blocks & 1 Pair - Network*

Data Line Protector w/ Dual Terminal

Blocks & 2 Pair - Network*

* Specify Voltage

We manufacture Data Line Protectors for any type of connection and

pin configuration. Please call for prices and delivery.

Specifications

• Voltage: 5V to 200V A/C or P/C	• Power Dissipation: 1st stage: 5,000 AMP
	• Current: Non-load bearing (voltage sensitive)	 Power Dissipation: 2nd stage: Filter
	• Clamping Point: As required, normally just above	• Power Dissipation: 3rd stage: 100,000 VA 8 x 20
	 maximum - Normal voltage, i.e. 5V clamp at 6V	• Connectors: As required
	 Response Time: <5 Nanoseconds

Risc 6000 Protectors

The female is the unprotected side and the male is the protected. The male side

should go toward the equipment to be protected. The external screw is for the

ground - 12 or 14 gauge stranded wire should be used for grounding.

Risc 6000 Surge Suppressors

R6000/64-DB9

R6000/64-RJ45

R6000/64-DB9, RJ45

R6000/128-HDI5

Risc 6000 - 64 Port w/ DB9M/F Connectors

Risc 6000 - 64 Port w/ RJ45M/F Connectors

Risc 6000 - 64 Port w/ DB9 M - RJ45 F

Risc6000- l28Portw/HD15M/F

Connectors

Surge Suppressors

# Text boxes

Specification for RISC 6000

• Standoff Voltage: 15 Volts

• Capacitance: <100 P.F.

• External ground on outside of box

• Follow-on Current: None

• Max Protection: 100,000 VA @ 8 x 20jis

• Resistance: >10 meg ohm to

ground

• Operation Temperature: -650C

- 1750C

• Clamping Time: <5 Nanoseconds

• Connectors: RJ45 M/F, DB9 M/F,

HDI5 MIF, or DB9 MIRJ45F