IsoShield

## Provides isolation of long-line digital, analog, control and telco circuits of 5v – 90v

Prevent failures and downtime before they occur.

Low voltage line isolator, stabilizer

# And cross strike protector:

Purpose:

To eliminate voltage differential and grounding differential.

Isolate and protect against ground loop failures.

Isolates against Lightning induced transits.

Provides applied corrective voltage regulation on the output.

Green LED Indicates proper Polarity for DC Circuits

Red LED Indicates reverse Polarity for DC circuits

Red LED indicates Ring Generation (AC) on “dial-up lines” and proper operation for all models.

Red/Green LED Indication represents (AC)

Reason:

Sensitive electronics, telco, alarm and telemetry systems often require an “isolator” to eliminate transient  impulses, ground loop currents and line loss problems.  All too often conventional surge suppression devices, being transient voltage activated, can’t correct these problems because they allow continuous and surge currents to pass by.  Often thermal fuses and MOVs prove too slow in response to protect surface mount components with low pf values.  The IsoShield can correct these problems and increase signal readings accuracy by providing; 1. transient suppression, 2. line isolation and 3. source voltage regulation.  Thus system operation can be more accurate, repeatable, fault tolerant and more reliable.

Example Performance:

Most analog signal and telemetry feedback devices operate at 24 VDC (in theory).  However, the applied 24 volts is subject, over distance, to impedance and other devices loading the line to where voltage drop often exceeds 5 or 6 volts.  This is an indicator that high surge currents and/or current loops will cause problems to accurate readings and cause failures during lightning storms or magnetically induced surges. The IsoShield breaks these currents by “isolation” and provides each device “source voltage regulation.” With an input as low as 19 volts the IsoShield outputs a regulated 24 volts to the devices. Performance, repeatability, and reliability are improved.  Lightning “blow-out” is avoided because there is no reference to ground on either side of the IsoSheild. Voltage differentials that cause false alarms thus eliminated.

# Text boxes

Gnd

Stormin Protection Products, 10749 63rd Way N, Pinellas Park, FL.  33782  |  888-471-1038  |  Storminprotection@att.com Storminprotection@att.com

Device

Iso  Shield

Signal Source or

Feedback Reader

DC Power

Supply

Models:

Iso2wTB-5V Data    (Optional Dinrail mountable)

Iso2wTB-16V Data

Iso2wTB-24V Data

Iso2wTB-24V Audio

Iso2wTB-48V Data

Iso2wTB-48V Audio

Iso2wTB-90V Audio

Iso2wTB-90VAC Data, Audio & Dial-up

Excellent for:

RS485

RS422

Audio Circuits including stereo

Telephone Lines

Short hall  Modems

Telemetry

Custom Controls.

Excellent for:

- RS-485

- RS-422

- Audio Circuits, Stereo

- Telephone Lines

- Short hall  Modems

- Telemetry

- Custom Controls.

Patent Pending