Primary Telephone & Modem Surge Protection

Telephone - Single Stage

DLT 1P (XXX)**     Telephone System Protector - 1 Pair

DLT 2P (XXX)**     Telephone System Protector - 2 Pair

DLT 3P (XXX)**     Telephone System Protector - 3Pair

DLT 4P (XXX)**     Telephone System Protector - 4 Pair

RURJ 11/2W            Ring Up Modem RJ 11 Standard

Connector - I Pair

RU RJ 14/4W	Ring Up Modem
RU RI 31	Ring Up Modem

Standard units available in 15V, 30V, 60V, 200V

Specify Voltage Required

20		Surge Suppressors

Click here for Index                                               Click here for Page 19                                            Click here for Page 21

# Text boxes

Specifications for Telephone - Single Stage

# Connects to the M-66 Telco Block

# Other voltages available on request

• Voltage Available: 15V, 30V, 60V & 200V for Ring-up

lines

• Response Time: 5 Nanoseconds

• Non Load-Bearing/Voltage

• No follow - on current

• Single Stage - 400,000 VA Protection per pair @ 8 x 20~is

• Instant Reset/Long Life

• Dimensions: 3” x 1 ½” x 1”

Telephone - Three Stage

DLT T0S DTB (XXX)**	Telephone System Protector

DLT TOS 200V

200 Volt Telephone System

Protector - PTSU/RSTU

Printed Circuit Board Cards

for Toshiba, Panasonic, or SMT Hybrid Phone Systems

** Specify Voltage Required

(XXX = I5V, 30V, 60V, 200V)

Specifications for Telephone -

## Three-Stage Hardwire

• Connection:	Terminal Board or RJ11
• Technology:	Hybrid Circuitry
	Multi-Stage Design
	Full Heat sinking
• Response:	< 5 Nanoseconds
• Operating Temperature:	-400C - ±850C
• Voltage:	Voltage Sensitive
• Current:	Non Load-Bearing
	No Follow -On Current
• Clamping Point:	15, 30, 60, 200 Volts or
	Special
• Power Dissipation:	2,000,000 Volt Amps
	4,000.000 Volt / Line Pair
• Lines Protected:	l Pair

• Tested to ANSI/IEEE B-3 Impulse

UL 497 listed