Specifications for Telephone - Two Stage

Punch down to the M-66 Telco Block, Screw down to telco Jacks, Hardwired to

Residential screw terminal block out side of home or office building.

Voltage Available: 15V, 30V,60V & 200 V for Ring-up lines

Voltage available for open loops: iSV, 30V for signal lines.

Response Time: <5 Nanoseconds

Non Load-Bearing/Voltage	
	No follow - on current	
	Two stage, diodes and MOV - 400,000 VA Protection per pair @ 8x2Ous	
	Instant Reset/Long Life

Dimensions:	3”xl.S”xl”

CO-IP (XXX)	Telephone System protector - 1 Pair
	CO-2P (XXX)	Telephone System Protector - 2 Pair
	CO-3P (XXX)	Telephone System Protector - 3 Pair
	CO-4P (XXX)	Telephone System Protector - 4 Pair
	CO-6P (XXX)	Telephone System Protector - 6 Pair
	CO-8P (XXX)	Telephone System Protector - 8 Pair

XXX Standard units available in 15V, 30V, 60V, 200 V....Specified Voltage Required

PHONE: 1-888-471-1038

jpecore@earthlink.net

http://www.storminprotection.com

# Text boxes

Color Codes

Per pair

Red /Green

Yellow! Black

White! Blue

14 gage Copper

Green wire for

Ground

Stormin Protection Products Inc.

10749 63rd Way N.

Pinellas Park, FL.  33782

Toll Free: 1-888-471-1038

Phone: 727-548-5418

Fax: 727-548-0867