Dedicated Modem Protectors

Dedicated Modem Protectors

RU RJ 45/4W	Dedicated Modem - 2 Pairs Protected*
RU RJ 4 1/45 8W	Dedicated Modem - 4 Pairs Protected*
RU RJ 48S	Dedicated Modem - 2 Pairs Protected*
RU RJ 45S	Dedicated Modem - 2 Pairs Protected*
D-4W-TB	Dedicated Modem - 2 Pairs Protected*

Auto Dialers/Burglar Alarms

Surge Suppressors	17

# Text boxes

Dedicated Modem Protector

• Dedicated Modem Protector w/ 4-position

terminal board input, 4-wire output w/

Telephone Co. color code & ground nut on

side of case.

• Protector is high-energy absorbing arrestor

/ 3-stage wI redundant circuitry I capable of

absorbing 5K amp strike in primary &

100,000 VA in secondary to insure

protection of equipment.

• Unit is not affected by temperatures from -

400C - + 800C

• Fully Encapsulated

• Pass Voltage: 5 volts to 200 volts*

• Dimensions: 3”H x 2”W x 1 112”D

This Product can be made in RJ45, and RJ11,

This Product is normally sold in lots of 10.

In lots of 20 Shipping will be included at no extra charge.

# DSL- Pacifier

In-line Series three Stage Hybrid RJ31X.   EMI/RFI filtering for DSL, pumps, motors, HVAC and other electromechanical devices that can cause false alarms due to excess generated frequency or Noise.  This is not just a filter, this is also a high end 600 joule three stage  Surge Suppressor.

Screw type Rj31X Jack, UL listed communications circuit assembly 82x6 E134135.  Meets FCC Part 68,50 Micron gold pins.  Protected pins 1,4,5,and 8.  Clamping voltage 130 VAC.  Response time is 5 nanoseconds or less.  Power dissipation is 240,000 VA 8x20us per pair protected.

Protection: UL1414 - E163321 	UL 1449 - E159095

CSA - LR103477-1

Electrical Parameters:

Three Stage protection, 		Hybrid In-Series Design

Response time 			1 Pico second

Breakdown voltage 		144-176 volts

Max Allowable voltage		AC: 130 V, DC: 170V

Varistor voltage: Vma: 		180V-220 at 1ma DC

Rated Wattage: 			.025 Watts

Withstanding Surge Current: 	(1) time: 1200A wave form 				8x20us, (2) times: 600A 					wave Form: 8x20us

Max Energy: Joules: 		86.3 Joules  : 10/1000us

Capacitance: 			310pf  Freq.: 1KHZ

Leakage Current: 		<20 uA 170VDC

Surge Life: 	1MA+ 10% 8x20us: 10000 times: 50A