Auto Dialers/Burglar Alarms

Surge Suppressors	17

# Text boxes

There is now more then one way to provide convenient Surge Protection for a burglar panel.  It has been suggested that we provide low voltage AC or DC protection on the RJ31X.  The Cost will determine the level of protection and DSL filtering.  Min order 10 or10 Mix

This Product can be made in RJ45, and RJ11,

This Product is normally sold in lots of 10.

In lots of 20 Shipping will be included at no extra charge.

# DSL- Pacifier

In-line Series three Stage Hybrid RJ31X.   EMI/RFI filtering for DSL, pumps, motors, HVAC and other electromechanical devices that can cause false alarms due to excess generated frequency or Noise.  This is not just a filter, this is also a high end 600 joule three stage  Surge Suppressor.

Screw type Rj31X Jack, UL listed communications circuit assembly 82x6 E134135.  Meets FCC Part 68,50 Micron gold pins.  Protected pins 1,4,5,and 8.  Clamping voltage 130 VAC.  Response time is 5 nanoseconds or less.  Power dissipation is 240,000 VA 8x20us per pair protected.

Protection: UL1414 - E163321 	UL 1449 - E159095

CSA - LR103477-1

Electrical Parameters:

Three Stage protection, 		Hybrid In-Series Design

Response time 			1 Pico second

Breakdown voltage 		144-176 volts

Max Allowable voltage		AC: 130 V, DC: 170V

Varistor voltage: Vma: 		180V-220 at 1ma DC

Rated Wattage: 			.025 Watts

Withstanding Surge Current: 	(1) time: 1200A wave form 				8x20us, (2) times: 600A 					wave Form: 8x20us

Max Energy: Joules: 		86.3 Joules  : 10/1000us

Capacitance: 			310pf  Freq.: 1KHZ

Leakage Current: 		<20 uA 170VDC

Surge Life: 	1MA+ 10% 8x20us: 10000 times: 50A

$35.00 each case of 10 = $350 + s/h

$35.00 each case of 20= $700 + Free S/H

First time order, min 3 units $75.00 + 6 s/h

## RJ31XA

Single Stage RJ31X protection only $21.00

## RJ31XB

Two Stage Protection RJ31X $26.00

RJ31XDSL

DSL Pacifier Three Stage protector $30.50

## RJ31XA12V  /  RJ31XA24V

Single Stage RJ31X protection w 12 or 24 V AC or DC Protection only $25.50 ea.

### RJ31XB12V  /  RJ31XB24V

Two Stage RJ31X protection w 12 or 24 V AC or DC Protection only $30.50 ea.

RJ31XDSL12V / RJ31XDSL24V

DSL Three Stage RJ31X protection w 12 or 24 V AC or DC Protection only $35.00ea.

Single outlet  $9.00 ea. Lots of 10

Separate