Security & Access Control

Security/Access Control

# Video Cameras/Monitors/Satellite Dish

Page23

# Text boxes

KP5/ S-G 		Key Pad - 5 lines & Shield Protected w/

Ground Lug

CR 5/S-G		Card Reader-5 Lines & Shield protected w/

Ground Lug

D2WDTB		Loop Lines - 1 Pair Protected

D4WDTB		Loop Lines - 2 Pair Protected

D 2W DTB-G		Loop Lines - 1 Pair Protected w/ Ground Lug

D4WDTB-G		Loop Lines - 2 Pair Protected w/ Ground Lug

D6WDTB/G		Hoop lines - 3 Pair Protected w/ Ground Lug

RU RI 31X-Kit		Telephone Line Protector - includes 1DLT

1 P 200V and Hard wire Connector block w/

Female RJ3JX connector

RURJ 31X-HE		Telephone Line Protector - RU/RJ 31X Plugs

High Energy Model

CCTV BNC V		Video Coax WI Female BNC in & out*

CCTV BNCC V		Video Coax w/ Female BNC in & male out*

CCTVF-CONN		Video Coax WI Female “F”in & out*

CCTV C/F		Video Coax w/ Female “F”in & male out*

TRI-AX-BNC		Video Triax w/ Female BNC in & out +3 outlets*

TRI-AX-F		Video Tñax w/ Female ‘F’ in & out +3 outlets*

CATV 24V AC		24V AC Camera Power Protector

CATVD 24VTB		24V DC Camera Power Protector

P1250P			Pelco Pan/Tilt 1250P Series

PT 680-24P		Pelco Pan/Tilt PT680-24P Series

PT 680-24SL		Pelco Pan/Tilt PT680-24SL Series

Ddual2WDTB/G		RS485 Pan/Tilt Zoom 2 wire

Ddual4WDTB/G		RS422 Pan/Tilt Zoom 4 wire

CCTV RCA		Video Coax w/2 female F “in” & 2 male “out”

* All Coax protectors for CATV or CCTV

Specifications for Pan/Tilt Protectors

•	4,556,000 VA Surge Suppression @ 8 x 20us

•  560 Joules of protection / 280 Joules - Pan, 280 Joules-Tilt

•	Reaction Time: <5 Nanoseconds

•	Non load-bearing (voltage sensitive)

•   Follow-on Current: None

•   Protects: Leg/Leg, Leg/Common, Common/ Ground

•  Unit size 3” x 2” x11/2” Easy fit in pan/tilt)

• Completely encapsulated for weatherproof operation

• Color coded to Pelco color codes

## CCTV/CATV/Coax Protector Specifications

•  Clamping Point; 2V

•	Response Time: <5 Nanoseconds

•  Power Dissipation: Hybrid Circuitry/Multi-Stage/ Full

Heatsinking

•  Operating Temperature: - 400C - + 850C

•  Current: Non Load-Bearing! No Follow-on Current

•  Voltage: Voltage sensitive

•  Insertion Loss: <dB at 100 pf

•  Operating Environment: Weatherproof

•  Connectors: BNC or F

•  Tested to ANSI/IEEE Standards

### OVERVOLTAGE PROTECTION DEVICE PRODUCT WARRANTY

LIFETIME LIMITED WARRANTY STATEMENT

Stormin Protection Products, Inc., hereafter referred to as SPPI, Inc., warrants its products, including but not limited to those manufactured to specification supplied to it for lifetime to the original retail purchaser. SPPI, Inc., assumes no risk or liability for the results of the use of products purchased from it, including but without limiting the generality of the foregoing:

Unsuitability of any product for use in any circuit or assembly. Purchasers rights under this warranty shall consist solely of requiring SPPI, Inc., to repair or, at SPPI, Inc., sole discretion, to replace free of charge, FOB. Factory, any defective items received at said factory and determined by SPPI, Inc., to be defective. The giving of or failure to give any advice or recommendations by SPPI, Inc., shall not constitute any warranty by or impose any liability on SPPI, Inc. The foregoing constitutes the sole and exclusive liability of SPPJ, Inc. AND IS IN LIEU OF ANY AND ALL OTHER WARRANTIES, EXPRESS, IMPLIED OR STATUTORY AS TO THE MERCHANT ABILITY, FITNESS FOR PURPOSE SOLD, DESCRIPTION, QUALITY PRODUCTIVENESS, and OR ANY OTHER MATTER. In no event shall SPPI, Inc. be liable for special or consequential damages or for delay in performance of this warranty.

Page32													Surge Suppressors