# Text boxes

Stormin Protection Products Inc.

10749 63rd Way N.

Phone: 1-888-471-1038

jpecore@earthlink.net

Pinellas Park, FL.  33782

Toll Free: 1-888-471-1038

Phone: 727-548-5418

Fax: 727-548-0867

# Specifications - Operating

Maximum Operating Voltage				5 Volts, 16 Volts, 24 Volts, 48 Volts, 200V

Typical Leakage Current					<5u Amps

Maximum Data Rate					22K, 56K, 128K, 1.5 Mb, 10 Mb

Operation Temperature					0 to 85 c

Connectors						Dual Terminal Blocks

Lines protected						1 pairs, 2 pairs, & 3 pairs

Dimensions for 2 pair & 3 pairs				3” x 2” x 1 1/2” + (Terminals 1/2’, Ground screw 1/2”)

Dimensions for 1 pair					1” x 2” x 1 1/2” + (Terminals 1/2”, Ground screw 1/2”)

Tabs, for mounting					1 1/2”

# Specifications - Electronic

Maximum Surge Current (8x20us)				3000 Amps Total

Maximum Surge Voltage (1.2X50us)			6000 Volts

Capacitance						<120pf to 12pf depending on Data Rate.

Clamping Voltage					5 Volts, 16 Volts, 24 Volts, 48 Volts, 200 Volts

Clamping Response Time					<5 Nanoseconds

Current							3 ohms, to non Load Bearing, depending on application.

Voltage							Voltage Sensitive

Pass Voltage Tested to ANSI/IEEE B3 Impulse		8 Volts, 18 Volts, 34 Volts, 60 Volts, 238 Volts

1st Stage Power Dissipation (8x20us)			5000 Amps per line

2nd Stage Series 						(-) negative coafficiant resister

3rd Stage Power Dissipation				Diodes, 100,000 Volt Amps

Jouls							560 Jouls with all three stages for 22K, 56K, 128K

Jouls							200 Jouls with two stage for 128K, 1.5Mb, 10 Mb

Stormin Surge Suppressors have a Lifetime Product Warranty

DDUAL4WDTB/G

DDUAL6WDTB/G

DDUAL2WDTB/G