# Text boxes

Frequency:

Phase Numbers

Voltage Scope

Frequency

Meter

Single-Phase

110V

60Hz +- 10%

Electronic Diognostics

Out Put

Modular

Replace-

able

Power Factor

Voltage Stabilized degrees

Translation Time

Capacity

Power

Surrounding Temperature

Surrounding humidity

Weight

Size

Housing

Battery

+ADDITIONAL BATTERY+

UPON REQUEST

COSF= 0.6

+-10%

<10ms

500 Va or 389 Watts

90%

0-40

< 90%

18 lbs

5.25” H x 8” D x 19 L

Fire Retardant Plastic

(1)     7Ah 12 Volt battery 15 min.

(2)    8Ah 12 Volt Battery 40 min.

1000VA Run Time Capasity

# Coax BNC Modular Replaceable

CCTV BNC Coax Surge Suppression

16 BNC inputs——16 BNC output

Maximum Operation Voltage– 7.5V

Typical Leakage Current- <5u amps

Maximum Insertion Loss- <1 dB

Operation Temp.– 0 to 85 C

Connectors– BNC or F Connectors

Max Surge Current– 500 amps

Max Surge Voltage– 6000 Volts

Capacitance- < 60pf

Clamping Response Time < 5 Nano

Current– Non Load Bearing

Voltage– Voltage Sensitive

Pass Volt Test ANSI/IEEE B3 impulse < 15 V Peak

Power Dissipation– 100,000 VA

(note) It could have RJ45 Cat 5, UHF connectors, RS485 or 422 Screw Terminals Replaceable modules

Phone: 888-471-1038

http://www.storminprotection.com

Surge

Suppression

Modular

Replaceable

UL 1449 2nd edition with thermal fusing & UL 497A  for RJ11.

Three Stage Hybrid Tank Circuit design

AC Outlets 6-R15 (8) Outlets.

Protection Modes– P/N, P/G, N/G

Max Surge Current rating 96,000 Amps total.

Max Surge Voltage– 20,000 Volts

Clamping Voltage– 130 Volts RMS

Clamping Response Time- 5 nanoseconds

Max Line Amperage 15A @ 120V AC

Voltage Sensitive, Noise Filter Response time 1 picoseconds EMI/RFI Dual Three Stage Filter.

Operation & Ground Indicator LED

Power Dissipation-840 Joules or 8,906,000VA

Audiable Alarm & Redundent on/off switch

Stormin Protection Products Inc.

jpecore@earthlink.net

10749 63rd Way N

Pinellas Park, FL.  33782

Toll Free: 1-888-471-1038

Phone: 727-548-5418

Fax: 727-548-0867

CCTV BNC Coax Surge Suppression

16 BNC inputs——16 BNC output

Maximum Operation Voltage– 7.5V

Typical Leakage Current- <5u amps

Maximum Insertion Loss- <1 dB

Operation Temp.– 0 to 85 C

Connectors– BNC or F Connectors

Max Surge Current– 500 amps

Max Surge Voltage– 6000 Volts

Capacitance- < 60pf

Clamping Response Time < 5 Nano

Current– Non Load Bearing

Voltage– Voltage Sensitive

Pass Volt Test ANSI/IEEE B3 impulse < 15 Volts Peak

Power Dissipation– 100,000 VA

Retail $550.00

Extra Battery $100.00

Extra Battery $100.00

Retail $1100.00

You Can Customize or Add-On Your Own Low Voltage Protection. Approx $69.95 List, depending on Item.