Click on Index		Click on Page 37			Click on Page 39

# Text boxes

Stormin Protection Products Inc.

10749 63rd Way N.

Pinellas Park, FL.  33782

Toll Free: 1-888-471-1038

Phone: 727-548-5418

Fax: 727-548-0867

Warranty

Stormin’s surge suppressors have a lifetime Product Warranty.  Please see warranty statement for complete product warranty information.

Stormins CATV 24VAC line surge suppressor incorporates state-of the-art technology and provides multiple elements of protection for your sensitive video equipment.  Tested to ANSI/IEEE B ringwave standards that exceed normal UL 497 B testing standards by 90 times.  Unlike other AC Low Voltage line surge suppressors, Stormins CATV24VAC  line surge suppressor does employ hybrid technology.  Stormins CATV24VAC line is self restoring after each surge with ratings.  Stormins CATV24VAC protector does have a ground wire, or lug that will ground to the camara transformer AC ground. Stormins CATV24VAC surge suppressor is design to obsorb the surge line to line, and line to ground.

SPECIFICATIONS OPERATING

Maximum Operating Voltage.......

Typical Leakage Current.............

Operation Temperatures.............

Connectors................................

SPECIFICATIONS OPERATING

Maximum Operating Voltage.......

Typical Leakage Current.............

Operation Temperatures.............

Connectors................................

24 Volts

<5u amps

0 to 85 C

Hardwired.

2 Black leads & Green ground wire

Maximum Surge Current (8 x 20 us)..........

Maximum Surge Voltage (1.2 x 50 us)........

Capacitance..............................................

Clamping Voltage.....................................

Clamping Response Time..........................

Current...................................................

Voltage....................................................

Pass Volt Tested ANSI/IEEE B3 Impulse...........

Power Dissipation (8 x 20 us)....................

500 Amps Total

6,000 Volts

<12.0 pf

30 Volts

<5 nanoseconds

Non Load Bearing

Voltage Sensitive

<30 Volts Peak

250,000 Volt Amps

# Specification Electronics

DISTRIBUTED BY:

Page 27