# Text boxes

Stormin Protection Products Inc.

10749 63rd Way N.

Pinellas Park, FL.  33782

Toll Free: 1-888-471-1038

Phone: 727-548-5418

Fax: 727-548-0867

Coaxial Cable Line Surge Suppressor

# CCTV/ RCA

Stormin CCTV/RCA  coaxial digital line surge suppressor incorporates state-of-the-art technology and provides multiple elements of protection for your sensitive video equipment.  Tested to ANSI/IEEE B ringwave standards that exceed normal UL497 B testing standards by 90 times.  Unlike other video line surge suppressors, the Stormin CCTV/RCA coaxial video line surge suppressor does not employ MOV technology and will not cause high insertion loss on your coax lines.  The Stormin CCTV /RCA coaxial digital/video line is self restoring after each surge within ratings.

Specifications Operating

Maximum Operating Voltage			24 volts

Typical Leakage Current				>5u amps

Maximum Insertion Loss		         		> 1dB

Operation Temperatures			          	0 to 85 degrees

Maximum Surge current (8 x 20us)			500 Amps Total

Maximum Surge Voltage (1.2 x 50su)		6,000 Volts

Capacitance 						24 pf

Clamping Response Time				>5 nano

Current						Non Load Bearing

Voltage						Voltage Sensitive

Cable							RG6 or RG7