# Convenient Laptop AC and Modem Protection             Retail Cost $19.95 each

Dealer (10 units) Volume (25 Units) & Distributor (50Unit) Discounts available.

# Stormin Custom AC Plug-In Surge Suppressor – 1P-RJ11

The 1PRJ11 surge suppressor provides 1 AC outlet and 2 RJ11 Females for telephone, fax or modem protection.  This unit incorporates state-of-the-art technology and provides excellent protection for your electronic equipment with a maximum current draw of 15 amps and provides both common and normal noise filtering.  The 1PRJ11 is UL 1449 2nd edition. It has 340 volt peak pass voltage rating tested at IEEE spec level, which is 6,000 volts @ 3,000, amps, where as the UL test for these are 6,000 volts @ 500 amps.

# Specifications - Operating:

Maximum Operating Voltage:				120 Volts AC

Operation Temperature:					-40 to +85 C

Protection AC Modes:						Line/Neutral, Line/Ground, Neutral/Ground

Protection Telephone Modes:                                                 Tip & Ring

Maximum Surge Current (8x20us):				3,000 Amps

Maximum Surge Voltage (1.2x50us):				6,000 Volts

Clamping Voltage:						130 Volts RMS or 340V Peak let through Voltage

Clamping Response Time:					<1 Nanosecond

Maximum Line Amperage:					15 Amps @ 120 VAC 60Hz

Voltage:      							Voltage Sensitive

Response Time:                                                                      < 5 Nano Seconds

EMI/RFI Dual-Full 3 Stage Noise Filter:			40dB down - 10 KHz to 10 MHz

Noise Filter Response:					< 1 Pico Second (active)

Operation Indicator LED:					Yes

Power Dissipation (8x20us):					18,000,000 VA

Failure Mode:							Fails Safe (open)

Warranty							Life Time Replacement Warranty

# Text boxes

Stormin Protection Products Inc.

10749 63rd Way N.

Pinellas Park, FL.  33782

http://www.storminprotection.com

jpecore@earthlink.net

Toll Free: 1-888-471-1038

Phone: 727-548-5418

Fax: 727-548-0867